## Slide 1
Doyal Sarker, Tajnuba Hasan, Tri Ngo, Tuhin Das
Department of Mechanical and Aerospace Engineering
University of Central Florida (UCF)
Presented by: Doyal Sarker
Mechanical and Aerospace Engineering
University of Central Florida
October 03, 2023
Causality-Free Modeling of a Floating Wind Turbine Semisubmersible Platform with Validation Results

## Slide 2
Presentation Outline
Background
Model Overview
Hydrodynamics Modeling
Results Validation and Discussions
Conclusion and Future Work

## Slide 3
Background
Floating Offshore Wind Turbines (FOWTs)
Hydrodynamics modeling
CRAFTS: Control-oriented, Reconfigurable, and Acausal Floating Turbine Simulator
Modelica language for component-level modeling and simulation
Causality-Free Modeling
Plug and Play the component
Reuse and swapping
Independent direction of flow explicitly
Control-co-design idea

## Slide 4
[1] Allen, Christopher, et al. Definition of the UMaine VolturnUS-S reference platform developed for the IEA wind 15-megawatt offshore reference wind turbine. No. NREL/TP-5000-76773. National Renewable Energy Lab.(NREL), Golden, CO (United States); Univ. of Maine, Orono, ME (United States), 2020.
Model Overview
VolturnUS-S reference floating platform [1]
Top level model in CRAFTS
Optimized TMD installed in outer column (OC)
1DOF translation in vertical direction
Tower
RNA

## Slide 5
[2] Viswanathan, Savin, and Christian Holden. "Modelica Component Models for Non-diffracting Floating Objects and Quasi-static Catenary Moorings." Proceedings of the American Modelica Conference 2020, Boulder, Colorado, USA, March 23-25, 2020. Liu Electronic Press, 2020.
Hydrodynamics Modeling
Hydrodynamics Load
Linear
Non-Linear
Excitation
Radiation
Viscous-Drag
Potential Flow theory
Morison equation
Applicability:
D/L<0.2: Long wavelength approximation
KC > 2: Flow separation becomes dominant
D/L > 0.2: Diffraction becomes important
Wave-Excitation and Radiation problem [2]

## Slide 6
Hydrodynamics Modeling
Added Mass
Wave-Exc
Viscous Drag
[B] = Additional damping matrix
i,j = Surge (1), Sway (2), Heave (3), Roll (4), Pitch (5), Yaw (6); HS = Hydrostatic, ME = Morison Equation, LD = Linear Damping, SL = Submerged Length
Water depth
Water density
Submerged Volume
Wave Model
Body Kinematics
Floating Structure
Instantaneous body kinematics
Floater 6 DOF responses, mooring tensions, tower motions in Time/Frequency Domain)
Iterative Process

## Slide 7
Wave Modeling and Assumptions
Linear Airy Wave Theory
JONSWAP Wave Spectrum
Hydrodynamics Assumptions
Small displacement approximation in hydrostatic load formulation
Added mass and drag coefficient don’t vary with water depth
Incident wave amplitudes are much smaller than the wavelengths
Irregular waves are modeled superimposing several linear regular waves.

## Slide 8
Validation Results
Simulation Setup
No aerodynamic loads
Global reference fixed at SWL
Water density 997.2 kg/m3
Water depth 350 m
Time step 0.05 sec
Column discretization, n = 100
Pontoon discretization, n = 10
Load Cases (LCs)
Load Cases (LCs) |  |  | Wave Conditions
LC1.X | -- | Equilibrium | Still Water
 | 1.1 | Surge static offset | Still Water
 | 1.2 | Heave static offset | Still Water
 | 1.3 | Pitch static offset | Still Water
LC2.X | 2.1 | Surge free decay | Still Water
 | 2.2 | Heave free decay | Still Water
 | 2.3 | Pitch free decay | Still Water
LC3.X | 3.2 | Fixed TMD | Irregular Wave
 | 3.5 | Pitch TMD | Irregular Wave
 | 3.8 | Tower TMD | Irregular Wave

## Slide 9
Validation Results
LC1.X (Equilibrium and Static offset tests)
DOF | OpenFAST | CRAFTS
Surge (m) | 3.19 | 3.19
Sway (m) | -1.97 | -1.97
Heave (m) | 0.02 | 0.02
Roll (deg) | -0.46 | -0.49
Pitch (deg) | -0.21 | -0.19
Yaw (deg) | 0.02 | 0.02
MLT: Mooring Line Tension
Prescribed position imposed in six DOFs.
Linear relationship

## Slide 10
Validation Results
LC2.X (Free decay tests)
Natural Period Damping
Small phase shift in Pitch motion
Sway period: 4.14 % higher than experiment
Logarithmic decrement (Damping)

## Slide 11
Validation Results
LC3.2 (Fixed TMD), Irregular Wave (Hs = 10.9 m, Tp = 14.2 sec, β = 0 deg)
Significant motions: Surge, Heave, Pitch
Analysis: Power spectral density (PSD)
Frequency (Hz)
Frequency (Hz)
TMD1 (Downwind, +Y)
TMD2 (Downwind, -Y)
TMD3 (Upwind, -X)

## Slide 12
Validation Results
LC3.5 (Pitch TMD), Irregular Wave (Hs = 10.9 m, Tp = 14.2 sec, β = 0 deg)
, TMD tuned to pitch frequency
Pitch TMD Strokes
Frequency (Hz)
Frequency (Hz)
 | Experiment | OpenFAST | CRAFTS
Pitch resonance | 19 % | 40 % | 26 %

## Slide 13
Validation Results
LC3.8 (Tower TMD), Irregular Wave (Hs = 10.9 m, Tp = 14.2 sec, β = 0 deg)
, TMD tuned to tower 1st bending mode
Tower TMD Strokes
Frequency (Hz)
Frequency (Hz)
 | Experiment | OpenFAST | CRAFTS
Tower resonance | 65 % | 72 % | 78 %

## Slide 14
Conclusions and Future works
Developed a hydrodynamics module in CRAFTS library
Control co-design: controller and substructure were designed concurrently
Hydrodynamics module used strip theory-based Morison equation
TMDs were tuned to attenuate the platform’s pitch and tower bending resonance
Results were verified and validated against Experiments and OpenFAST results.
Focus on improving the hydrodynamics model accuracy
2nd order waves will be incorporated in the wave models
Real time spatial effect (Fluid-Structure Interaction) will be modeled properly
The floating platform will be integrated with actual wind turbine model
Active control needs to be incorporated.

## Slide 15
Thank You